## Slide 1: SPHEREx Calibration Lab Automation
Sam Condon, Howard Hui, Marco Viero

## Slide 2: Goals
Lab setup to automate:
  Spectral Calibration.
  Measurement of Telescope Focus and Error.
File Storage:
  Compressed but easily retrievable.
  Appropriate metadata in headers and easy to search.

## Slide 3: Direction
Plan is to have a GUI (QT) interface for a central codebase that drives all the instrumentation and data collection.
Preferably in Python (making every effort to avoid Labview).

## Slide 4: General Setup
Python
Libraries
OS
USB
USB Hub/FPGA/RSC Chain/ Labjack
Device
Device
Device
Device
Detector Readout
Metadata
Big Data

## Slide 5: Spectral Response
Light Source On
Shutter
Monochromator λ
Order Sorting Filter Wheel
Attenuating Filter Wheel
Power Meter
Cold Shutter
Detector Array
Write to DataFrame
Merge Metadata/ Compress
Write to RAID

## Slide 6: Telescope Focus
Laser On
Move Pinhole
Write to Disk
Merge Metadata/ Compress
Write to RAID
Microscope Calibration
Collimator Calibration
Focus Measurement
Measure Spot Size
Move Camera
Measure Spot Size
Laser On
Move Camera
Measure Spot Size
Measure Spot Size
Insert Pinhole
Move Pinhole
Blackbody On
Move Pinhole
Measure PSf

## Slide 7: Spectral Response
Device | COM | Library/ Driver | Passive/ Active | Manual/ Automated | Metadata | Big Data
Thorlabs Light Source | n/a | n/a | passive | manual | no | no
Oriel Monochromator | USB 2.0 | Oriel C++ API, C#.NET, pyVISA | active | automated | yes | no
Power Meter | USB 2.0 | SCPI, pyVISA, pySerial | passive | automated | yes | yes
Oriel Filter Wheel | Ribbon to Monochro-meter | Monochrometer Control | passive | automated | yes | no
NDF Wheel | USB 2.0/ RS232 | pySerial | passive | automated | yes | no
Cold Shutter | TTL | Arduino/pySerial | passive | automated | no | no
Readout Electronics | ? | ? | ? | ? | yes | yes
Active means something that changes between each frame/file.

## Slide 8: Telescope Focus
Device | COM | Library/ Driver | Passive/ Active | Manual/ Automated | Metadata | Big Data
Laser | n/a | n/a | passive | manual | no | no
FLIR CCD Camera | GigE | Spinnaker SDK/OpenCV | passive | automated | yes | yes
Microscope | RS-485 | pySerial | active | automated | yes | no
Velmex XY Stages | RS-485 | pySerial | passive | automated | yes | no
Velmex Linear Stage | RS-485 | pySerial | active | automated | yes | no
Heidenhain Gauge | EnDat 2.2/ RS-485 | pySerial? | passive | automated | yes | yes
Newmark Gimbal | RS-485 | pySerial | passive | automated | yes | no
Thorlabs Blackbody | n/a | n/a | passive | manual | no | no
Readout Electronics | ? | ? | ? | ? | yes | yes
Stepper Motors (Anaheim Motor Driver)
Active means something that changes between each frame/file.

## Slide 9: Timeline
Action | Feb |  | March |  |  |  | April |  |  |  | May |  |  |  | June |  |  |  | July |  |  | 
Finalize Plans |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Lab Cleanup |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Spectral Calibration |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Develop HW wrappers |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Develop Codebase |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Assemble Optics |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Test Runs |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Integrate Cryostat |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Focus |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Develop HW wrappers |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Develop Codebase |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Assemble Optics |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Develop Automation |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Test Runs |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Integrate Cryostat |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
KASI CHAMBER ARRIVES

## Slide 10: What’s happening right now
Lab cleanup is underway. Urgency level? How can we expedite?
Sam is going through each component to determine how we will communicate with it.
Marco is researching efficient ways to approach the master codebase.
Lab Communication Channels
Slack Channel: #calibration-lab
Github Repository: SPHEREx/SPHEREx-lab-tools

## Slide 11: Choices to be made
Command hardware via USB hub, FPGA, Labjack, Arduino, (other?), or some combination?
Data storage format (.csv, .avro, .parquet?)
Problems to Solve
Can we integrate the Oriel Monochromator specific USB drivers into the pyVISA framework and thus avoid using the Oriel provided C++ API?
Stepper motors all driven by Anaheim Driver realistic?
Which FLIR camera are we using?